## Slide 2: Flynn’s Taxonomy of Computers
Mike Flynn, “Very High-Speed Computing Systems,” Proc. of IEEE, 1966
SISD: Single instruction operates on single data element
SIMD: Single instruction operates on multiple data elements
  Array processor
  Vector processor
MISD: Multiple instructions operate on single data element
MIMD: Multiple instructions operate on multiple data elements (multiple instruction streams)
  Multiprocessor
  Multithreaded processor
Notes: Ask predicated executions
Use image as an exmaple. Load one million pixels.

## Slide 3: Data Parallelism
Concurrency arises from performing the same operations on different pieces of data
  Single instruction multiple data (SIMD)
  E.g., dot product of two vectors
Contrast with data flow
  Concurrency arises from executing different operations in parallel (in a data driven manner)

## Slide 4: SIMD Processing
Single instruction operates on multiple data elements
  In time or in space
Multiple processing elements
Time-space duality
  Array processor: Instruction operates on multiple data elements at the same time
  Vector processor: Instruction operates on multiple data elements in consecutive time steps

## Slide 5: Array vs. Vector Processors
ARRAY PROCESSOR
VECTOR PROCESSOR
LD VR  A[3:0]
ADD VR  VR, 1
MUL VR  VR, 2
ST A[3:0]  VR
Instruction Stream
Time
LD0
LD1
LD2
LD3
AD0
AD1
AD2
AD3
MU0
MU1
MU2
MU3
ST0
ST1
ST2
ST3
LD0
LD1
AD0
LD2
AD1
MU0
LD3
AD2
MU1
ST0
AD3
MU2
ST1
MU3
ST2
ST3
Space
Space
Same op @ same time
Different ops @ same space
Different ops @ time
Same op @ space
Notes: The array processors are more expensive.
GPU has both

## Slide 6: SIMD Array Processing vs. VLIW
VLIW

## Slide 7: SIMD Array Processing vs. VLIW

## Slide 8: Vector Processors
A vector is a one-dimensional array of numbers
Many scientific/commercial programs use vectors
    for (i = 0; i<=49; i++)
    C[i] = (A[i] + B[i]) / 2
A vector processor is one whose instructions operate on vectors rather than scalar (single data) values
Basic requirements
  Need to load/store vectors  vector registers (contain vectors)
  Need to operate on vectors of different lengths  vector length register (VLEN)
  Elements of a vector might be stored apart from each other in memory  vector stride register (VSTR)
    Stride: distance between two elements of a vector
Notes: Why do we need vector processors? Many scientific codes perform operations on arrays.
For the last item, show C = A * B. We load a row of A and a column of B.

## Slide 9: Vector Processors (II)
A vector instruction performs an operation on each element in consecutive cycles
  Vector functional units are pipelined
  Each pipeline stage operates on a different data element
Vector instructions allow deeper pipelines
  No intra-vector dependencies
  No control flow within a vector
  Known stride allows prefetching of vectors into cache/memory

## Slide 10: Vector Processor Advantages
+ No dependencies within a vector
  Pipelining, parallelization work well
  Can have very deep pipelines, no dependencies!
+ Each instruction generates a lot of work
  Reduces instruction fetch bandwidth
+ Highly regular memory access pattern
  Interleaving multiple banks for higher memory bandwidth
  Prefetching
+ No need to explicitly code loops
  Fewer branches in the instruction sequence

## Slide 11: Vector Processor Disadvantages
-- Works (only) if parallelism is regular (data/SIMD parallelism)
++ Vector operations
-- Very inefficient if parallelism is irregular
-- How about searching for a key in a linked list?
Fisher, “Very Long Instruction Word architectures and the ELI-512,” ISCA 1983.

## Slide 12: Vector Processor Limitations
-- Memory (bandwidth) can easily become a bottleneck, especially if
1. compute/memory operation balance is not maintained
2. data is not mapped appropriately to memory banks
Notes: Talk about operations per memory load

## Slide 13: Vector Processing in More Depth

## Slide 14: Vector Registers
Each vector data register holds N M-bit values
Vector control registers: VLEN, VSTR, VMASK
Maximum VLEN can be N
  Maximum number of elements stored in a vector register
Vector Mask Register (VMASK)
  Indicates which elements of vector to operate on
  Set by vector test instructions
    e.g., VMASK[i] = (Vk[i] == 0)
V0,0
V0,1
V0,N-1
V1,0
V1,1
V1,N-1
M-bit wide
M-bit wide

## Slide 15: Vector Functional Units
Use deep pipeline (=> fast clock) to execute element operations
Simplifies control of deep pipeline because elements in vector are independent
V1
V2
V3
V3 <- v1 * v2
Six stage multiply pipeline

## Slide 16: Vector Machine Organization (CRAY-1)
CRAY-1
Russell, “The CRAY-1 computer system,” CACM 1978.
Scalar and vector modes
8 64-element vector registers
64 bits per element
16 memory banks
8 64-bit scalar registers
Notes: Fastest scalar component

## Slide 17: Memory Banking
Memory is divided into banks that can be accessed independently; banks share address and data buses
Can start and complete one bank access per cycle
Can sustain N parallel accesses if they go to different banks
Bank
0
Bank
1
MDR
MAR
Bank
2
Bank
15
MDR
MAR
MDR
MAR
MDR
MAR
Data bus
Address bus
CPU
Notes: MDR: memory data register
MAR: memory address register
One bank needs 11 cycles to complete, how many banks do you need?

## Slide 18: Vector Memory System
0
1
2
3
4
5
6
7
8
9
A
B
C
D
E
F
+
Base
Stride
Vector Registers
Memory Banks
Address Generator
Notes: We can allocate A[0] to bank 0, A[1] to bank 1. Is it the best way? What if we have A[2*i]? It depends on the access pattern.

## Slide 19: Scalar Code Example
For I = 0 to 49
  C[i] = (A[i] + B[i]) / 2
Scalar code (instruction and its latency)
  MOVI R0 = 50 1
  MOVA R1 = A 1
  MOVA R2 = B 1
  MOVA R3 = C 1
  X: LD R4 = MEM[R1++] 11 ;autoincrement addressing
  LD R5 = MEM[R2++] 11
  ADD R6 = R4 + R5 4
  SHFR R7 = R6 >> 1 1
  ST MEM[R3++] = R7 11
  DECBNZ --R0, X 2 ;decrement and branch if NZ
304 dynamic instructions
Notes: 11 is the num. of cycles

## Slide 20: Scalar Code Execution Time
Scalar execution time on an in-order processor with 1 bank
  First two loads in the loop cannot be pipelined: 2*11 cycles
  4 + 50*40 = 2004 cycles
Scalar execution time on an in-order processor with 16 banks (word-interleaved: consecutive words are stored in consecutive banks)
  First two loads in the loop can be pipelined
  4 + 50*30 = 1504 cycles
Why 16 banks?
  11 cycle memory access latency
  Having 16 (>11) banks ensures there are enough banks to overlap enough memory operations to cover memory latency

## Slide 21: Vectorizable Loops
A loop is vectorizable if each iteration is independent of any other
For I = 0 to 49
  C[i] = (A[i] + B[i]) / 2
Vectorized loop:
  MOVI VLEN = 50 1
  MOVI VSTR = 1 1
  VLD V0 = A 11 + VLN - 1
  VLD V1 = B 11 + VLN – 1
  VADD V2 = V0 + V1 4 + VLN - 1
  VSHFR V3 = V2 >> 1 1 + VLN - 1
  VST C = V3 11 + VLN – 1
7 dynamic instructions

## Slide 22: Basic Vector Code Performance
Assume no bypassing (no vector data forwarding)
  i.e., output of a vector functional unit cannot be used as the direct input of another
  The entire vector register needs to be ready before any element of it can be used as part of another operation
One memory port (one address generator)
16 memory banks (word-interleaved)
285 cycles
Notes: Chaining: pass data of one vector processing unit to another vector processing unit

## Slide 23: Vector Chaining
Vector chaining: Data forwarding from one vector functional unit to another
Memory
V1
Load Unit
Mult.
V2
V3
Chain
Add
V4
V5
Chain
LV v1
MULV v3,v1,v2
ADDV v5, v3, v4
Slide credit: Krste Asanovic

## Slide 24: Vector Code Performance - Chaining
Vector chaining: Data forwarding from one vector functional unit to another
182 cycles
These two VLDs cannot be
pipelined. WHY?
VLD and VST cannot be
pipelined. WHY?
Notes: We have only one port, which is why for the last operation, we should wait until the previous load finishes.

## Slide 25: Vector Code Performance – Multiple Memory Ports
Chaining and 2 load ports, 1 store port in each bank
79 cycles

## Slide 26: Questions
What if # data elements > # elements in a vector register?
  Need to break loops so that each iteration operates on # elements in a vector register
    E.g., 527 data elements, 64-element VREGs
    8 iterations where VLEN = 64
    1 iteration where VLEN = 15 (need to change value of VLEN)
  Called vector stripmining
What if vector data is not stored in a strided fashion in memory? (irregular memory access to a vector)
  Use indirection to combine/pack elements into vector registers
  Called scatter/gather operations

## Slide 27: Gather/Scatter Operations
Want to vectorize loops with indirect accesses:
  for (i=0; i<N; i++)
  A[i] = B[i] + C[D[i]]
Indexed load instruction (Gather)
  LV vD, rD # Load indices in D vector
  LVI vC, rC, vD # Load indirect from rC base
  LV vB, rB # Load B vector
  ADDV.D vA,vB,vC # Do add
  SV vA, rA # Store result
Notes: When do we need indirect accesses? Graph applications. Say hello to neighbors example.

## Slide 28: Gather/Scatter Operations
Gather/scatter operations often implemented in hardware to handle sparse matrices
Vector loads and stores use an index vector which is added to the base register to generate the addresses
Index Vector Data Vector Equivalent
0 3.14 3.14
2 6.5 0.0
6 71.2 6.5
7 2.71 0.0
0.0
0.0
71.2
2.71

## Slide 29: Conditional Operations in a Loop
What if some operations should not be executed on a vector (based on a dynamically-determined condition)?
  loop: if (a[i] != 0) then b[i]=a[i]*b[i]
  goto loop
Idea: Masked operations
  VMASK register is a bit mask determining which data element should not be acted upon
  VLD V0 = A
  VLD V1 = B
  VMASK = (V0 != 0)
  VMUL V1 = V0 * V1
  VST B = V1
  Does this look familiar? This is essentially predicated execution.

## Slide 30: Another Example with Masking
for (i = 0; i < 64; ++i)
if (a[i] >= b[i]) then c[i] = a[i]
else c[i] = b[i]
A B VMASK
1 2 0
2 2 1
3 2 1
4 10 0
-5 -4 0
0 -3 1
6 5 1
-7 -8 1
Steps to execute loop
1. Compare A, B to get
VMASK
2. Masked store of A into C
3. Complement VMASK
4. Masked store of B into C

## Slide 31: Masked Vector Instructions
C[4]
C[5]
C[1]
Write data port
A[7]
B[7]
M[3]=0
M[4]=1
M[5]=1
M[6]=0
M[2]=0
M[1]=1
M[0]=0
M[7]=1
Density-Time Implementation
  scan mask vector and only execute elements with non-zero masks
C[1]
C[2]
C[0]
A[3]
B[3]
A[4]
B[4]
A[5]
B[5]
A[6]
B[6]
M[3]=0
M[4]=1
M[5]=1
M[6]=0
M[2]=0
M[1]=1
M[0]=0
Write data port
Write Enable
A[7]
B[7]
M[7]=1
Simple Implementation
  execute all N operations, turn off result writeback according to mask

## Slide 32: Some Issues
Stride and banking
  As long as they are relatively prime to each other and there are enough banks to cover bank access latency, consecutive accesses proceed in parallel
Storage of a matrix
  Row major: Consecutive elements in a row are laid out consecutively in memory
  Column major: Consecutive elements in a column are laid out consecutively in memory
  You need to change the stride when accessing a row versus column

## Slide 33: Array vs. Vector Processors, Revisited
Array vs. vector processor distinction is a “purist’s” distinction
Most “modern” SIMD processors are a combination of both
  They exploit data parallelism in both time and space

## Slide 34: Remember: Array vs. Vector Processors
ARRAY PROCESSOR
VECTOR PROCESSOR
LD VR  A[3:0]
ADD VR  VR, 1
MUL VR  VR, 2
ST A[3:0]  VR
Instruction Stream
Time
LD0
LD1
LD2
LD3
AD0
AD1
AD2
AD3
MU0
MU1
MU2
MU3
ST0
ST1
ST2
ST3
LD0
LD1
AD0
LD2
AD1
MU0
LD3
AD2
MU1
ST0
AD3
MU2
ST1
MU3
ST2
ST3
Space
Space
Same op @ same time
Different ops @ same space
Different ops @ time
Same op @ space

## Slide 35: Vector Instruction Execution
ADDV C,A,B
C[1]
C[2]
C[0]
A[3]
B[3]
A[4]
B[4]
A[5]
B[5]
A[6]
B[6]
Execution using one pipelined functional unit
C[4]
C[8]
C[0]
A[12]
B[12]
A[16]
B[16]
A[20]
B[20]
A[24]
B[24]
C[5]
C[9]
C[1]
A[13]
B[13]
A[17]
B[17]
A[21]
B[21]
A[25]
B[25]
C[6]
C[10]
C[2]
A[14]
B[14]
A[18]
B[18]
A[22]
B[22]
A[26]
B[26]
C[7]
C[11]
C[3]
A[15]
B[15]
A[19]
B[19]
A[23]
B[23]
A[27]
B[27]
Execution using four pipelined functional units

## Slide 36: Vector Unit Structure
Lane
Functional Unit
Vector
Registers
Memory Subsystem
Elements 0, 4, 8, …
Elements 1, 5, 9, …
Elements 2, 6, 10, …
Elements 3, 7, 11, …
Slide credit: Krste Asanovic

## Slide 37: Vector Instruction Level Parallelism
Can overlap execution of multiple vector instructions
  example machine has 32 elements per vector register and 8 lanes
  Complete 24 operations/cycle while issuing 1 short instruction/cycle
load
load
mul
mul
add
add
Load Unit
Multiply Unit
Add Unit
time
Instruction issue

## Slide 38: Automatic Code Vectorization
for (i=0; i < N; i++)
C[i] = A[i] + B[i];
load
load
add
store
load
load
add
store
Iter. 1
Iter. 2
Scalar Sequential Code
Vectorization is a compile-time reordering of operation sequencing
 requires extensive loop dependence analysis
Vector Instruction
load
load
add
store
load
load
add
store
Iter. 1
Iter. 2
Vectorized Code
Time

## Slide 39: Vector/SIMD Processing Summary
Vector/SIMD machines are good at exploiting regular data-level parallelism
  Same operation performed on many data elements
  Improve performance, simplify design (no intra-vector dependencies)
Performance improvement limited by vectorizability of code
  Scalar operations limit vector machine performance
  Amdahl’s Law
  CRAY-1 was the fastest SCALAR machine at its time!
Many existing ISAs include (vector-like) SIMD operations
  Intel MMX/SSEn/AVX, PowerPC AltiVec, ARM Advanced SIMD

## Slide 44: Sample GPU SIMT Code (Simplified)
for (ii = 0; ii < 100000; ++ii) {
C[ii] = A[ii] + B[ii];
}
// there are 100000 threads
__global__ void KernelFunction(…) {
int tid = blockDim.x * blockIdx.x + threadIdx.x;
int varA = aa[tid];
int varB = bb[tid];
C[tid] = varA + varB;
}
CPU code
CUDA code

## Slide 46: Sample GPU Program (Less Simplified)

## Slide 47: Threads Can Take Different Paths in Warp-based SIMD
Each thread can have conditional control flow instructions
Threads can execute different control flow paths
Thread Warp
Common PC
Thread
2
Thread
3
Thread
4
Thread
1
B
C
D
E
F
A
G

## Slide 48: Control Flow Problem in GPUs/SIMT
A GPU uses a SIMD pipeline to save area on control logic.
  Groups scalar threads into warps
Branch divergence occurs when threads inside warps branch to different execution paths.
Branch
Path A
Path B
Branch
Path A
Path B
This is the same as conditional execution.
Recall the Vector Mask and Masked Vector Operations?

## Slide 49: Branch Divergence Handling (I)
Idea: Dynamic predicated (conditional) execution
-
G
1111
TOS
B
C
D
E
F
A
G
Thread Warp
Common PC
Thread
2
Thread
3
Thread
4
Thread
1
B/1111
C/1001
D/0110
E/1111
A/1111
G/1111
-
A
1111
TOS
E
D
0110
E
C
1001
TOS
-
E
1111
E
D
0110
TOS
-
E
1111
A
D
G
A
Time
C
B
E
-
B
1111
TOS
-
E
1111
TOS
Reconv. PC
Next PC
Active Mask
Stack
E
D
0110
E
E
1001
TOS
-
E
1111
Slide credit: Tor Aamodt

## Slide 50: Branch Divergence Handling (II)
A
B
C
D
A
--
1111
B
D
1110
C
D
0001
Next PC
Recv PC
Active Mask
D
--
1111
Control Flow Stack
One per warp
A;
if (some condition) {
B;
} else {
C;
}
D;
TOS
D
1
1
1
1
A
0
0
0
1
C
1
1
1
0
B
1
1
1
1
D
Time
Execution Sequence
Slide credit: Tor Aamodt

## Slide 51: Dynamic Warp Formation/Merging
Idea: Dynamically merge threads executing the same instruction (after branch divergence)
Form new warps from warps that are waiting
  Enough threads branching to each path enables the creation of full new warps
Warp X
Warp Y
Warp Z

## Slide 52: Dynamic Warp Formation/Merging
Idea: Dynamically merge threads executing the same instruction (after branch divergence)
  Fung et al., “Dynamic Warp Formation and Scheduling for Efficient GPU Control Flow,” MICRO 2007.
Branch
Path A
Path B
Branch
Path A

## Slide 53: Dynamic Warp Formation Example
A
A
B
B
G
G
A
A
C
C
D
D
E
E
F
F
Time
A
A
B
B
G
G
A
A
C
D
E
E
F
Time
A
x/1111
y/1111
B
x/1110
y/0011
C
x/1000
y/0010
D
x/0110
y/0001
F
x/0001
y/1100
E
x/1110
y/0011
G
x/1111
y/1111
A new warp created from scalar threads of both Warp x and y executing at Basic Block D
D
Execution of Warp x
at Basic Block A
Execution of Warp y
at Basic Block A
Legend
A
A
Baseline
Dynamic
Warp
Formation
Slide credit: Tor Aamodt